## Slide 1: Canny edge detection – fpga speedup
David watts
Max dunevitz

## Slide 2: Canny Edge Detection
A multi-stage image edge detection algorithm developed by John Canny in 1986
The algorithm involves two main steps
  Calculation and comparison of the intensity gradients of pixels to locate edges
  Hysteresis thresholding of the gradient magnitudes of pixels to refine the edge detection and suppress “weaker” edges

## Slide 3
Example of a processed image

## Slide 4: Full Algorithm Overview
Notes: Max, on this slide I would like to circle the parts that software does and what part the FPGA will be responsible for

## Slide 5: Project Overview
To speed up the Non-maximal Suppression (NMS) and thresholding steps of the algorithm by processing these steps on hardware using an FPGA
Process
  Calculation of the gradients is performed in software
  The gradient magnitudes and directions are passed to the FPGA
  FPGA performs NMS and thresholding and returns a binary image to the user
Note that the hysteresis thresholding is simplified to a simple binary threshold against a single value
Processing time in software and hardware are compared to calculate the speedup

## Slide 6: Project Process
TODO
Notes: Max, on this slide I would like to circle the parts that software does and what part the FPGA will be responsible for

## Slide 7: Software implementation
The algorithm is coded using C++ coupled with the OpenCV libraries in software
Gradient magnitudes and directions are calculated, then output to a CSV file
The CSV file is loaded to the server which parses it and writes entries to the FPGA
The FPGA processes the data and the binary image is returned in a reverse manner

## Slide 8: Software flow
TODO
Notes: Max, on this slide I would like to circle the parts that software does and what part the FPGA will be responsible for

## Slide 9: Software output

## Slide 10: Hardware Datapath
Datapaths created for the NMS and thresholding blocks
NMS block
  Input: Magnitudes (8-bit integers) of all pixels in a 3x3 square and the direction (3-bit integer) of the center pixel
  Output: single bit indicating that the pixel is kept (1) or suppressed (0)
Thresholding block
  Input: Magnitude of the center pixel
  Output: single bit indicating that the pixel passes (1) or fails (0) the threshold

## Slide 11: Non-maximal suppression
TODO

## Slide 12
NMS Block A
NMS Block B
Thresholding Block

## Slide 13: memory mapping
3 input RAM’s
Each RAM contains N-1 rows of pixels from the input image (N is number of rows in image)
  CPU will be writing identical data to each RAM with some offset
  This allows us to “unroll” the datapath 3 times
  With unrolling, there is a 3 cycle latency to fill the buffer

## Slide 14: Hardware flow
Notes: Max, on this slide I would like to circle the parts that software does and what part the FPGA will be responsible for

## Slide 15: Image recreation glitch
How software recreated image
What it should look like

## Slide 16: Example outputs

## Slide 17: Example outputs

## Slide 18: Thresholding sensitivity
Lower level
Higher level