## Slide 1: Canny edge detection – fpga speedup
David watts
Max dunevitz

## Slide 2: Software implementation
Using OpenCV libraries to accomplish Canny Edge Detection in C++
Currently does hysteresis thresholding too, but take out later
Fully functional

## Slide 3: Software output

## Slide 4: Software with hardware STEPS
Notes: Max, on this slide I would like to circle the parts that software does and what part the FPGA will be responsible for

## Slide 5: Current progress: memory mapping
3 input RAM’s
Each RAM contains N-1 rows of pixels from the input image (N is number of rows in image)
  CPU will be writing identical data to each RAM with some offset
  This allows us to “unroll” the datapath 3 times
Software can now write 16-bit magnitude and 16-bit angle for each pixel

## Slide 6: Current Progress: Datapath
Writing base datapaths for non-maximal suppression (NMS) and thresholding
  Synthesize and test with a single iteration (no unrolling)
  Implement unrolling for greater speedup
NMS block
  Input: Magnitudes (8-bit integers) of all pixels in a 3x3 square and the direction (3-bit integer) of the center pixel
  Output: single bit indicating that the pixel is kept (1) or suppressed (0)
Thresholding
  Input: Magnitude of the center pixel
  Output: two bits indicating that the pixel is passes (1) or fails (0) the high/low thresholds

## Slide 7
NMS Block A
NMS Block B
Thresholding Block

## Slide 8: Current Progress: Datapath
TODO
  NMS to thresholding linkage implementation
  Datapath-to-memory and linkage
  Pixel magnitude and direction conversion (from 16-bit to 8- and 3-bit integers)